## Slide 1
Vision Projects
Operations Technology
Sujith Muraleedaran

## Slide 2
VISION PROJECTS (Plan & Status)
S.No | Project | Plant | Start Date | End Date | Current Status | Capex Cost | ROI
1 | Multiguaging - OCR Part No Identification | P.Palayam - Stellantis | 08.08.2025 | 18.11.2025 | Completed | 7,34,000 | 4.6 months
2 | Keyence Laser Measurement | P.Palayam - Stellantis | 15.08.2025 | 08.01.2026 | Completed | 12,23,000 | 1.15 years
3 | MPI Crack Identification- Knowledge Q | P.Palayam - Daimler | 03.01.2026 | 01.03.2026 | Completed | 8,25,560 | 7.5 Months

## Slide 3
Multiguaging Final Inpection
Plant : P-palayam| Project : SFQA
1
Home

## Slide 4
Multiguaging Final Inpection with OCR based component Tracking System - Results
Plant : P-palayam| Project : SFQA
ROI Calculations - OCR part Identification
Parameter | Unit Cost | Value
Total Machines Used |  | 1
Total Camera Used |  | 1
Operators Required per Shift (Current) |  | 8
Total Operators Required per Day (Current) | 8 × 1 | 8
Salary per Operator per Month |  | ₹ 22,000
Current Monthly Manpower Cost | 8 × 22,000 | ₹ 1,76,000
Current Annual Manpower Cost | 1,76,000 × 12 | ₹ 21,12,000
Operators Required After Automation |  | 1
Monthly Manpower Cost After Automation | 1 × 22,000 | ₹ 22,000
Annual Manpower Cost After Automation | 22,000 × 12 | ₹ 2,64,000
Annual Savings Due to Automation | 21,12,000 − 2,64,000 | ₹ 18,48,000
Total Automation Project Cost |  | ₹ 7,34,000
ROI Payback Period (Years) | 7,34,000÷ 18,48,000 | 0.39 years
ROI Payback Period (Months) | 0.39 × 12 | 4.68 Months
Operator Reduction | 08 − 01 | 07 Operators Reduced
Savings After 5 Years | (18,48,000 × 5) − 7,34,000 | ₹ 58,66,000

## Slide 5
OCR-Based Component Tracking System
SC3000 OCR Camera — reads part number
MGPL Fixture — holds Oil Pump Sprocket
Display: 028.027 mm reading confirmed
OCR Measurement Station
Part-Wise Quality Report Dashboard
P-palayam

## Slide 6
OCR-Based Component Tracking System - Before vs After
P-palayam

## Slide 7
Multiguaging Final Inpection - Results
Plant : P-palayam| Project : SFQA

## Slide 8
Keyence Camera-Based Dimensional Measurement
Contact Gauging Limitations
Traditional contact gauges caused wear, required frequent calibration, and risked surface damage on precision Stellantis sprocket components.
No Simultaneous Multi-Param
Root Dia, OD, ID, Total Thickness and Teeth Distance had to be measured separately using different instruments — slow, error-prone, and operator-dependent.
Manual Measurement Variation
Operator-to-operator variation in measurements led to inconsistent quality records and false accept/reject decisions.
Problem Statement
Solution
P-palayam
2
Home

## Slide 9
ROI Calculations - Part Measurement project
Plant : P-palayam| Project : SFQA
Parameter | Calculation | Value
Total Gauges used |  | 5
Total Camera Used |  | 1
Operators Required per Shift (Current) |  | 5
Total Shifts per Day |  | 3
Total Operators Required per Day (Current) | 5 × 1 | 5
Salary per Operator per Month |  | ₹ 22,000
Current Monthly Manpower Cost | 5 × 22,000 | ₹ 1,10,000
Current Annual Manpower Cost | 1,10,000 × 12 | ₹ 13,20,000
Operators Required After OCR |  | 1
Monthly Manpower Cost After Automation | 1 × 22,000 | ₹ 22,000
Annual Manpower Cost After Automation | 22,000 × 12 | ₹ 2,64,000
Annual Savings Due to Automation | 13,20,000 − 2,64,000 | ₹ 10,56,000
Total Automation Project Cost |  | ₹ 12,23,000
ROI Payback Period (Years) | 12,23,000 ÷ 10,56,000 | 1.15 Years
ROI Payback Period (Months) | 1.15 × 12 | 13.8 Months
Operator Reduction | 5 − 1 | 04 Operators Reduced
Savings After 5 Years | ( 10,56,000 × 5) − 12,23,000 | ₹ 40,57,000

## Slide 10
Keyence Camera-Based Dimensional Measurement - Before vs After
P-palayam

## Slide 11
MPI Crack Detection Automation
P-palayam
3
Home

## Slide 12
MPI Crack Detection Automation - ROI calculation
P-palayam
Parameter | Calculation | Value
Total System used |  | 1
Total Camera Used |  | 1
Operators Required per Shift (Current) |  | 2
Total Shifts per Day |  | 3
Total Operators Required per Day (Current) | 2 × 3 | 6
Salary per Operator per Month |  | ₹ 22,000
Current Monthly Manpower Cost | 6 × 22,000 | ₹ 1,32,000
Current Annual Manpower Cost | 1,32,000 × 12 | ₹ 15,84,000
Operators Required After OCR |  | 1
Monthly Manpower Cost After Automation | 1 × 22,000 | ₹ 22,000
Annual Manpower Cost After Automation | 22,000 × 12 | ₹ 2,64,000
Annual Savings Due to Automation | 15,84,000 − 2,64,000 | ₹ 13,20,000
Total Automation Project Cost |  | ₹ 8,25,560
ROI Payback Period (Years) | 8,25,560 ÷ 13,20,000 | 0.625 Years
ROI Payback Period (Months) | 0.625 × 12 | 7.5 Months
Operator Reduction | 6 − 3 | 03 Operators Reduced
Savings After 5 Years | ( 13,20,000 × 5) − 8,25,560 | ₹ 57,74,440

## Slide 13
MPI Crack Detection Automation - LIVE AURONIQ SCREENS
P-palayam

## Slide 14
MPI Crack Detection Automation - ANALYTICS DASHBOARD & INSPECTION REPORT
P-palayam

## Slide 15
MPI Crack Detection Automation - Solution & Results
P-palayam

## Slide 16
MPI Crack Detection Automation - LIVE AURONIQ SCREENS
Plant : P-palayam| Project : SFQA

## Slide 17
Thank you